## Slide 1
Sound Wine Production
Essential Analysis
Avoiding Faults
January 17, 2025

## Slide 2: Production
  Lab Analysis
  Cleaning and Sanitation
  Fruit Quality
  Fermentation Management
  Racking and filtration
  Fining and Blending
  Bottling Procedures

## Slide 3: The Winery Laboratory
Building considerations
  Easily accessible from all processing areas
  Minimum 100 sq. feet
  Sink
  Sturdy table or counter
  Chemical storage
  Good ventilation
  Refrigerator

## Slide 4: Lab Equipment
Necessities:
  Refractometer/hydrometers
  pH meter
  Titration set-up (burette, burette stand)
  Ebulliometer
  Analytical balance
  SO2 measurement
  Several thermometers
  Asst. glassware (beakers, flasks, etc.)
Others
  Volatile acidity still, nephelometer, carbodoseur, spectrophotometer, others

## Slide 5: The Winery Laboratory
Flow chart establishes:
  Place of each analysis in the production scheme
  Time that results of each analysis are needed
  Level of accuracy and specificity for results
  Acceptable ranges for results
Allows the winemaker to formulate a proactive course of action if results fall outside of specified range.

## Slide 6: Analysis Flow Chart
From: Zoecklein, B.
Enology Notes #115

## Slide 7
Harvest | pH | Ta | Brix | Nitrogen | Sensory | Temperature
During Fermentation | Residual sugar | MLF | Sensory |  |  | Y
Post-fermentation | pH | Ta | Free SO2 | Sensory |  | Y
Post- cold stabilization | pH | Ta | Free SO2 | Alcohol | Sensory | Y
Trouble shooting | VA | Fining trials | Aroma Screen | Stability tests | Sensory | Y
Post adjustment | pH | Ta | Free SO2 | Alcohol | Sensory | Y
Pre-bottling | Free SO2 | Sensory |  |  |  | Y

## Slide 8: Faults
  Oxidation
  Sulfur Compounds
  Spoilage yeasts
  Cork taint
  Geranium taint
  LAB
  Harvest
  Brix
  pH
  Titratable Acidity (TA)
  Post Fermentation
  Alcohol, pH, TA, Free SO2
  Residual Sugar
  Heat Stability, Cold Stability
  Organoleptic assessment
Analysis

## Slide 9
  “ It’s not what you look at that matters, it’s what you see.”
  H D Thoreau
  “ Knowledge is knowing a tomato is a vegetable, Wisdom is knowing not to put it in a fruit salad.”
  Brian O’Driscoll

## Slide 10: Fruit Quality
Subjective - Clean fruit free from disease and damage
Measurable - TA, Brix, pH
Subjective - Color, skin health
What’s the wine style?
Subjective - Flavor and taste

## Slide 11: Pre-Harvest Sanitation
The cleaning and sanitation of processing equipment pre harvest.
Using a detergent cleaner.
Using a sanitizing solution prior to equipment use.
Food grade lubricants
When cleaning for harvest tanks, hoses, clamps, gaskets, crusher, press, crush bins.

## Slide 12
Wineries can use ATP testing to monitor the cleanliness of critical points in the winemaking process. This can help them to optimize their cleaning & sanitation protocols, and to prevent quality problems before they arise.
ATP (adenosine triphosphate) levels in wineries are measured using a luminometer and a testing swab:
ATP is a molecule found in all living cells, including those in bacteria and yeast. The presence of ATP on a surface indicates that it is contaminated and may not have been cleaned properly. This could mean that the surface has food residue, allergens, or bacteria on it, and could potentially support bacterial growth.
Collect a sample: Use a swab to collect a sample from a surface in the winery
Analyze the sample: Insert the swab into the luminometer
Measure the ATP level: The luminometer produces a light output that is measured in relative light units (RLU)
Interpret the results: A higher RLU reading indicates a higher amount of ATP, which means more cells are present and the surface is less clean
Using an ATP Monitor

## Slide 13
Many brands available. Average cost $ 1700.00 - $ 2500.00 per unit.
Test Swabs $ 5.00 - 12.00 each.
Average cost of wine in bottle. $ 14.50 to $ 21.00. At $ 15.00 a bottle $ 180.00 a case.
Therefore, value of product in the case $ 75.71 gallon at 50.00 % GP $ 37.85.
Value at $ 1330.00 to replace if you are fortunate. (133 gal per pallet)
Understanding that something is clean prior to sanitation is key.
ATP Monitor

## Slide 14
Good winemaking practice is guiding microbial populations and closing the spoilage window

## Slide 15: Cleaning vs. sanitation
Winemaking is 1.00 % Science, 1.00 % Art, 1.00 % Common Sense
97.00 % Cleaning & Sanitation
Cleaning
  Physical removal of organic deposits
    Soil, solid particles, detritus
Sanitation
  Reduction of Microbes to safe levels, kill 99.99 %
    Applied post-cleaning
Sterilization
  Complete destruction of all Microbes

## Slide 16: Sanitation Options
Hot Water/Steam Sanitation
  Inexpensive and effective
    Cleaning, 100-140oF
    Sterilization, 180-200oF for 20 min.
  Sulfur Dioxide
  Ozone
  Quaternary Ammonia
  Many choices of cleaners and sanitizers, just ensure it works on your system.

## Slide 17: Fermentation Management
Clean equipment and solid juice / fruit.
Correct yeast selection, preferably one meant for wine.
Nutrient management and additions.
Appropriate brix adjustments.
Temperature control to maintain rates of fermentation.
Additions of Nutrient at 1/3 sugar depletion, make final addition before 10 brix.
Monitor Brix drops daily, adjust temperature as necessary.
With reds on skins keep the cap punched down or pumped over.

## Slide 19: Blending, Filtration, Fining
Racking post ferment, clean, then clean again, sanitize.
Blending of another wine can be the difference between OKAY and great.
Fining using tannins, proteins, yeast derivatives.
The process of fining can remove unwanted phenolics, off flavors.
- drifine, albuminicol, pea protein, Clarigel, oak tannin, skin tannin, hydroclar, to name a few.
You can use tannin to change a wine style soften or add age ability to a wine.
Filtration is an important step on the evolution of a wine. Pads, lenticular, cartridge, DE filtration, centrifuge.

## Slide 20
THANK YOU